## Slide 1
Wuqiong Luo
Chapter 5 Steady Electric Currents

## Slide 2
Starting from
Maxwell equations
Conditions
Constitutive relations
boundary conditions
Static electric field problems
Classification according to the charge static or motion
Electrostatic field
Steady current field
Static
Arbitrarily
Uniform motion
Finite
Chap 5

## Slide 3
Contents
5.1 Introduction
5.2 Current Density and Ohm’s Law
5.3 Electromotive Force and KVL
5.4 Equation of Continuity and KCL
5.5 Power Dissipation and Joule’s Law
5.6 Boundary Conditions for Current Density
5.7 Resistance Calculations

## Slide 4: 5.1 Introduction
There are several types of electric currents caused by the motion of free charges
Electrolytic currents (电解电流): migration of positive and negative ions.
Convection currents (运流电流): results from motion of positively or negatively charged particles in a vacuum or rarefied gas.
Conduction currents (传导电流) in conductors and semiconductor: drift motion of conduction electrons and/or holes.

## Slide 5
The amount of charge flowing across a given area per unit time is called the electric current intensity or electric current, and it is denoted by I. The unit of electric current is ampere (A), and its density is in Amperes per square meter. It is defined as,
5.2 Current Density and Ohm’s Law
s t
Where N is the number of charge per unit volume, is the velocity of charges, s is where the charges passing through.
density

## Slide 6
Current models in different distributions
Current models
Volumn current
Unit：A / m2 （安/米2）
1. Volumn current
movement direction of positive charge
unit cross section area
The corresponding total current is:
Surface current
d 0
2. Surface current
Unit：A / m
discussion:
3. line current

## Slide 7
In most conducting media, the conduction current density J at a point is proportional to the electric field intensity E at that point so that
Ohm’s law
Ohm’s Law
The above equations are valid only for a linear isotropic medium.
Differential form of Ohm’s law
Integral form
 : conductivity
conducting ability of the medium

## Slide 8
A conductor with infinite is called a
In a perfect electric conductor, electric current can be produced without the influence of an electric field.
There is no steady electric field in a perfect electric conductor. Otherwise, an infinite current will be generated, and it results in an infinite energy.

About 
P.E.C. （perfect electric conductor）
 →ꝏ
A medium without any conductivity is called a perfect dielectric or an insulator.
In nature there exists no any p.e.c. or perfect dielectric.
P.E.D. （perfect electric dielectric）
 →0

## Slide 9
The conductivities of several media
unit in S/m
Media | Conductivities | Media | Conductivities
Silver |  | Sea water | 
Copper |  | Pure water | 
Gold |  | Dry soil | 
Aluminum |  | Transformer oil | 
Brass |  | Glass | 
Iron |  | Rubber | 
conductivity

## Slide 10
The magnitude of the current density of the convection current is not proportional to the electric field intensity, and the direction may be different from that of electric field intensity.
If the charge density is  , and the moving velocity is v, and then
Convection current
Attention: convection current does not obey Ohm’s Law

## Slide 11
Characteristics of Steady current field
Q1: what are the physical quantities?
Q2: what characteristics of the quantities?

## Slide 12
The principle of conservation of charge is one of the fundamental postulates of physics. Electric charges may not be created or destroyed;
5.4 Equation of Continuity and KCL
Consider an arbitrary volume V bounded by surface S. A net charge Q exists within this region. If a net current I flows across the surface out of this region, the charge in the volume must decrease at a rate that equals the current;
Also, the current leaving the region is the total outward flux of the current density vector through the surface S;

## Slide 13
Assume the density of the sustained charges in the volume V bound by the closed surface S is , then
then
By using the divergence theorem, we obtain
which is called the principle of current continuity in differential form.
Chap 5.4

## Slide 14
Because the distribution of the charges in the steady electric current field is independent of time, i.e. , we find
which states that in the steady electric current field the flux of the current density through any closed surface will be zero.
Chap 5.4
which states that the steady electric current field is solenoidal.
With differential form,
Or KCL:

## Slide 15
The steady electric field caused by the sustained charges on the plates is also a conservative field, and the line integral of it around a closed circuit should be zero, i.e.
For homogeneous media, the above equation becomes
In the conducting medium,
Chap 5.4
with differential form:
In homogeneous conducting media the steady electric current field is irrotational.

## Slide 16
The work ∆w done by an electric field E in moving a charge q a distance is qE∙( ), which corresponds to a power
5.5 Power Dissipation and Joule’s Law
where u is the drift velocity. The total power delivered to all the charge carriers in a volume element d is
Power dissipation density

## Slide 17
This is known as Joule’s law.
For a given volume V, the total electric power converted into heat is
In a conductor of a constant cross section,
with measured in the direction J.
where I is the current in the conductor. Since V = RI, we have
Chap 5.5

## Slide 18
2. Boundary conditions (general problems)
Differential form ：
Constitutive relations：
1. Basic equations (general problems)
Integral forms ：
OR
3. Two types of problems according to the medium (special problems)
Conductive medium ：
Existing medium ：
5.6 Boundary Condition for Current Density

## Slide 19
The potential function satisfies the requirement of Laplace’s equations
of steady current field
Boundary conditions of electric potential

## Slide 20
two conductors
Medium and conductor
Direction relation of the field vector at the two sides of the interface
Boundary conditions on both sides of the boundary
The particularity of the field vector on both sides of the interface
conductor
medium
Conductive medium 2
Conductive medium 1
Surface charge ？
Is conductor equivalent electric potential ？
finite

## Slide 22
When will the steady current field be generated？
There is an electric field in a conducing medium！
The key is to find the electric field intensity
Based on the known charge
Based on current (Ohm's law) √
Based on electric potential √

## Slide 23
（1）The electric field intensity is expressed by the Ohm's Law ( constitutive relation of the conducing medium).
The method based on current to solve the problems of steady electric field
（2） The unknown quantity is expressed by a known quantity (usually the excitation voltage)

## Slide 24
Ex. A parallel plate capacitor consists of two imperfect dielectrics in series. Their permittivity are 1 and 2 , the conductivities are 1 and 2 , and the thickness are d1 and d2, respectively. If the impressed voltage is U, find the electric field intensities, the electric energies per unit volume, and the power dissipations per unit volume in two dielectrics.
Solution: Since no current exists outside the capacitor, the electric current lines in the capacitor can be considered to be perpendicular to the boundaries. Then we have
In view of this we find
 1 1
 2 2
d1
d2
U
Example

## Slide 25
The electric energies per unit volume in two dielectrics, respectively, are
The power dissipations per unit volume in two dielectrics, respectively, are
Two special cases are worth noting:
If , then , , , .
If , then , , , .
d1
d2
 1= 0
E 2= 0
U
E 1= 0
 2= 0
U
Example

## Slide 26
Ex. The voltage of inner conductor is U0, outer conductor is grounded.
Find:
(1) The current density and electric field in each region of coaxial line;
(2) The surface density of the free charge on the interface.
Example

## Slide 27
（1）The radial current in the coaxial cable is I ,
from the current density is
Electric field in medium 1
Solution: The current is flowing from the inner conductor to the outer conductor, only the normal component exists at the interface, so the current density is axial symmetrical distributed.
Current per unit length
Example

## Slide 28
Since
So
The current density and electric field inside two mediums:
Example

## Slide 29
The surface charge density on the outer surface of medium 2
The surface charge density between two conducting mediums
The surface charge density on the inner surface of medium 1
Example

## Slide 30
Resistance and conductance
5.7 Resistance Calculations
Method one of calculating conductance
Assuming the current between the two electrodes is I ；
For ，calculate the potential difference between two conductors
According to the definition of the conductance to calculate the conductance ：

## Slide 31
Method two of calculating conductance
Assuming the potential difference between the two electrodes is U ；
For ，find the current between two conductors
According to the definition of the conductance to calculate the conductance ：
Method three of calculating conductance
Electrostatic simulation ：

## Slide 32
Comparison between steady electric field and electrostatic field with electrostatic simulation method
Basic equations
electrostatic field （ area ）
Constitutive relations
Potential functions
boundary conditions
Steady electric field (outside the power supply)
Corresponding physical quantity
electrostatic field
steady electric
field

## Slide 33
Solution：
Resistance
Assume the current flowing from the inner conductor to the outer conductor is I.
Ex. The inner and outer radius is a 、b , length is l , the medium between has permittivity of ε and conductivity of σ. Find the resistance of coaxial line
Example

## Slide 34
Ex. A quarter of a flat circular conducting washer is shown in the figure. Calculate the resistance between two end faces.
U
y
x
t
a
b

r
0
(r,)
0
Solution: The cylindrical coordinate system should be selected. Assume the electric potential difference between two end faces is U, and let
Since the electric potential  is related to the angle , it should satisfy the following equation
The general solution is
The electric potential at
The electric potential at
Example

## Slide 35
Based on the given boundary conditions, we find
The current density J in the conducting medium is
Then the current I flowing into the conducting medium across the end face at is
Consequently, the resistance R between two end faces is
Example

## Slide 36
The general solution:
use B.C
then
Annular conducting medium
r1
h
r2
0
σ
Ex. Annular conducting medium with thickness of h and two radius of r1 and r2, has angle of  0 . The conductivity of the conductive medium is σ. find the resistance between the two electrodes along the  direction.
Solution: The voltage between two electrodes along  direction is U0, then current is flowing along  direction, and current density is changed with  . It is easy to determine that the potential  is just a function variables  , thus the potential function satisfies the one-dimensional Laplace equation
Example

## Slide 37
Current density
The current between two plates
So the resistance between two plates along  direction is:
So
Example

## Slide 38
一、Field is generated by static charge (electrostatic field)
The electric field is zero inside the conductor( )
The tangential electric field is zero on the surface of a conductor equal potential body
The charge is zero inside the conductor
Charge can only be located on the surface of the conductor, and it is concentrated in the sharp part of the surface.
Application: electrostatic induction, electrostatic shielding, lightning rod ，… …
Typical phenomena and conclusions of static electric field

## Slide 39
二、The DC electric field of the moving charge
(steady electric field)
There may be electric field inside the conductor( )
The tangential electric field is not zero on the surface of the conductor. Non equal potential body
There may be moving charge inside the conductor, but the net charge is zero.
Net charge can only be located on the surface of the conductor
The electric field and current inside the perfect conductor ( ), is zero .
Electric field on the boundary of ideal conductor is Perpendicular to the surface equal potential body
Typical electrostatic field

## Slide 40
Further understanding of the electrostatic field and steady electric field
QUESTIONS ：
conductor
U
Find：1） 2）Energy storage or power consumption?
conductor
w
t
ε
t
U

## Slide 41: Summary
1. Basic equations (general problems)
Constitutive relations：
2. Boundary conditions (general problems)
3. Resistance and conductance
electrostatic simulation method

## Slide 42: Summary
Constitutive relations：
1. Basic equations (general problems)
2. Boundary conditions (general problems)

## Slide 43: Homework
5-1, 5-6, 5-10, 5-15, 5-16, 5-22