## Slide 1: Power Electronics
DC-AC Converters (Inverters)
逆变器
Please read Chapter 8 in the textbook
Dr Atif Jafri
Atif.Jafri@glasgow.ac.uk

## Slide 2: Schemes of Inverters to study
Phase Output | Bridge | Switching Schemes | Operation in different switching schemes Output Waveform Harmonics Practical Circuit Avoiding shoot through
Single Phase | Half | Square Wave | 
 |  | Pules Width Modulation | 
 | Full | Square Wave | 
 |  | Pules Width Modulation (Bipolar & Unipolar) | 
Three Phase | 3-Leg | Square Wave | 
 |  | Pules Width Modulation | 
Half Bridge Studied in Last Lecture

## Slide 3: Schemes of Inverters to study
Phase Output | Bridge | Switching Schemes |  | Ideal Circuit Diagram Operation Output Waveform Harmonics Practical Circuit Diagram Avoiding shoot through
Single Phase | Half | Square Wave |  | 
 |  | Pules Width Modulation |  | 
 | Full | Square Wave |  | 
 |  | Pules Width Modulation |  | 
 |  | Bipolar | Unipolar | 
Three Phase | 3-Leg | Square Wave |  | 
 |  | Pules Width Modulation |  | 

## Slide 4: Inverter Types
Full Bridge Inverter (Ideal)
- Full Bridge
Figures used in the literature for Full Bridge Inverter
Full Bridge Inverter with Flyback Diodes

## Slide 5: Operation
- Square Wave Switching
Full Bridge Inverter (Ideal)

## Slide 6: Operation
Pulse Width Modulation (PWM) Switching - Bipolar
  Is a type of switching technique.
  Use two signals called
    (Triangular Signal)
      Has frequency (called switching frequency)
    (Control Signal)
      Has frequency (desired fundamental frequency)
v
v
v

## Slide 7: Operation
Pulse Width Modulation (PWM) Switching - Bipolar
  (Triangular Signal) is compared with (Control Signal)
  Based on comparison result different switches are made closed (ON) and open (OFF)
  Output voltage swings between positive and negative voltages
= +
Closed

## Slide 8: Operation
Pulse Width Modulation (PWM) Switching - Bipolar
  (Triangular Signal) is compared with (Control Signal)
  Based on comparison result different switches are made closed (ON) and open (OFF)
  Output voltage swings between positive and negative voltages
= -

## Slide 9: Operation
Pulse Width Modulation (PWM) Switching - Unipolar
  Is a type of switching technique.
  Use two signals called
    (Triangular Signal)
      Has frequency (called switching frequency)
    & (Control Signal)
      Has frequency (desired fundamental frequency)

## Slide 10: Operation
Pulse Width Modulation (PWM) Switching - Unipolar
  (Triangular Signal) is compared with &
  Based on comparison result different switches are made closed (ON) and open (OFF)

## Slide 11: Operation
Pulse Width Modulation (PWM) Switching - Unipolar
  (Triangular Signal) is compared with &
  Based on comparison result different switches are made closed (ON) and open (OFF)

## Slide 12: Operation

## Slide 13: Harmonics
What are harmonics?
  Pure Sinusoid is required.
  The output is different both in square-wave and PWM switching
  There is need to analyze the presence of other sinusoids having frequencies multiple of desired sinusoid, called harmonics, available in output.

## Slide 14: Harmonics
What are harmonics?
  Pure Sinusoid is required.
  The output is different both in square-wave and PWM switching
  There is need to analyze the presence of other sinusoids having frequencies multiple of desired sinusoid, called harmonics, available in output.
Output (PWM Switching - Bipolar)
Desired
Actual
Output (PWM Switching - Unipolar)
Actual
Desired
Output (Square Wave Switching)
Desired
Actual

## Slide 15: Harmonics
Harmonics in Square Wave Switching
  There is need to analyze the presence of other sinusoids having frequencies multiple of desired sinusoid, called harmonics, available in output.

## Slide 16: Harmonics
Harmonics in Square Wave Switching
  There is need to analyze the presence of other sinusoids having frequencies multiple of desired sinusoid, called harmonics, available in output.
Fourier Series Analysis

## Slide 17: Harmonics
Harmonics in PWM Switching
  To analyze “harmonics” for PWM switching we need to understand two new terms:
    Amplitude Modulation Ratio and Frequency Modulation Ratio.
v
v
v
Amplitude Modulation Ratio
Frequency Modulation Ratio
Peak Value of Control Signal
Peak Value of Triangular Signal
Frequency of triangular signal
also called switching frequency
Frequency of control signal also
called desired fundamental frequency

## Slide 18: Harmonics
Harmonics in PWM Switching (Bipolar)

## Slide 19
In the full-bridge converter circuit, = 300 V, = 0.8, = 39, and the fundamental frequency is 47 Hz. Calculate the rms values of the fundamental-frequency voltage and some of the dominant harmonics in the output voltage v, if a PWM bipolar voltage-switching scheme is used.

## Slide 20: Harmonics
Harmonics in PWM Switching (Unipolar)
Output (PWM Switching - Unipolar)
Actual
Desired

## Slide 21
In the full-bridge converter circuit, = 300 V, = 0.8, = 38, and the fundamental frequency is 47 Hz. Calculate the rms values of the fundamental-frequency voltage and some of the dominant harmonics in the output voltage v, if a PWM bipolar voltage-switching scheme is used.

## Slide 22: Harmonics
Comparing Harmonics
The Unipolar scheme has the advantage of “effectively” doubling the switching frequency as far as the output harmonics are concerned, compared to the bipolar voltage-switching scheme.
The advantage of “effectively” doubling the switching frequency appears in the harmonic spectrum of the output voltage waveform, where the lowest harmonics appear as sidebands of twice the switching frequency.
Harmonics
(Square Wave Switching)
Harmonics
(PWM Bipolar Switching)
Harmonics
(PWM Unipolar Switching)

## Slide 23: Practical Full Bridge Inverter
Made through real components
  Square Wave Switching
Avoiding
Shoot through
All switches on
Shoot Through

## Slide 24: Practical Full Bridge Inverter
Made through real components
  PWM Switching - Bipolar

## Slide 25: Practical Full Bridge Inverter
Made through real components
  Avoiding shoot through in PWM – Bipolar Switching
Causing Shoot Through
Additional of blanking time to avoid shoot through
Blanking Time

## Slide 26: Avoiding Shoot through
Blanking Time
  Avoiding shoot through in PWM – Bipolar Switching

## Slide 27: Practical Full Bridge Inverter
Made through real components
  PWM Switching - Unipolar

## Slide 28: To avoid shoot through in Unipolar two circuits made for Bipolar shall be used

## Slide 29: Comparison of different Schemes
 | Half Bridge ~ Full Bridge
Output Power Square Wave Switching | With the same dc input voltage, the maximum output voltage of the half-bridge inverter is half that of the full-bridge inverter. Hence, in case of low power applications we can use the half-bridge inverters and save one-leg of full bridge inverter.

## Slide 30: Comparison of different Schemes
 | Square Wave Switching | PWM Switching
Harmonics in Half or Full Bridge Inverter | The abrupt switching in square waves generates a significant number of harmonics. Harmonics are multiples of the fundamental frequency (the desired AC output frequency) that distort the waveform and can cause problems for connected equipment. | PWM uses a more sophisticated approach. It generates a pulse train with a constant frequency (carrier frequency) but varies the width of each pulse (duty cycle). By carefully controlling the duty cycle, PWM can effectively synthesize a sinusoidal output voltage. This approach "spreads out" the harmonics to higher frequencies, making them easier to filter.
 | To mitigate these harmonics and achieve a cleaner output waveform, square wave inverters need bulky and expensive filtering components. | As a result of this harmonic shaping, PWM inverters require smaller and more efficient filters to achieve the same level of output quality compared to square wave inverters.

## Slide 31: Comparison of different Schemes
 | Bipolar ~ Unipolar
Harmonics PWM Switching | In unipolar scheme, the advantage of “effectively” doubling the switching frequency appears in the harmonic spectrum of the output voltage waveform, where the lowest harmonics appear as sidebands of twice the switching frequency.

## Slide 32: Summary
Full Bridge DC-AC Converter studied with following switching option:
  Square Wave Switching
  PWM Bipolar Switching
  PWM Unipolar switching
following aspects were studied for each switching:
  Ideal Circuit Diagram
  Operation
  Output Voltage (Waveform)
  Harmonics
  Practical Circuit Diagram
  Avoiding shoot through
A comparison is made in different single-phase inverters.