## Slide 1
Wuqiong Luo
Chapter 2 Vector Analysis

## Slide 2
Contents
2.1 Vector algebra
2.2 Orthogonal Coordinate Systems
2.3 Gradient of a Scalar Field
2.4 Divergence of a Vector Field
2.5 Curl of a Vector Field
2.6 Solenoidal and irrotational fields
2.7 Laplacian Operations
2.8 Helmholtz’s Theorem

## Slide 3
2.1 Vector Algebra
1. Scalars and Vectors
Scalar：A quantity has only magnitude (Length, area, volume, temperature, density, energy…).
Vector：A quantity has both magnitude and direction (Force, displacement, velocity, acceleration, electric field intensity, magnetic field intensity…).
Fields：The distribution of a quantity in space will constitute a field. Hence, there are scalar fields and vector fields.

## Slide 4
1. Scalars and Vectors
Magnitude
of Vector：
Unit Vector：
Algebraic representation ：
Graphical representation of Vector：
A segment of a directed straight-line.
Thinking： Unit Vector = Constant Vector ?
Vector A
Constant Vector：with constant magnitude and fixed direction.
Vector algebra

## Slide 5
Vector in Cartesian Coordinates
z
x
y
Vector algebra

## Slide 6
（1）Addition and Subtraction of Vectors
2. Algebraic operation of vectors
Addition
Subtraction
Associative law
Commutative law
Vector algebra

## Slide 7
（2）A vector multiplied by a scalar
（3）Scalar product (dot product)
——Commutative law
q
Angle
Vector algebra

## Slide 8
（4）Vector product (cross product)
q
sin
AB
q
X
In components:
In determinant:
If ,then
Vector algebra

## Slide 9
（5）Vector Operations
—— Distributive law
—— Distributive law
—— Scalar triple product
—— Vector triple product
Prove them after class
Vector algebra

## Slide 10
Exercise：
1. Express in three components
2. Express in magnitude and phase
1. Result in value
2. Result in graph

## Slide 11: 2.2 Orthogonal Coordinate Systems
1. Cartesian Coordinates
Position
Surface element
Line element
Volume element
Variable
Unit vector
点
P(x0,y0,z0)
0
y
y
=
（plane）
o
x
y
z
0
x
x
=
（plane）
0
z
z
=
（plane）
P
x
y
z
o
d
z
d
y
d
x

## Slide 12
2. Cylindrical Coordinates
Variable
Unit vector
Position
Line element
Volume element
Surface element
Vector algebra

## Slide 13
Operation in cylindrical coordinate systems

## Slide 14
Exercise：
E.g. Calculte the integral of function f along the side surface of a cylinder with radius of 1, and height of h, where 。

## Slide 15
3. Spherical Coordinates
Variable
Unit vector
Position
Line element
Volume element
Surface element
Vector algebra

## Slide 16
E.g. Calculte the integral of function f on the surface of a sphere with radius of 1, where
Exercise：

## Slide 17
4. Relationships
Cartesian
and
Cylindrical
Cylindrical
and
Spherical
Cartesian
and
Spherical
o
f
x
y
Unit circle
Cartesian and cylindrical
f
o
q
r
z
Unit circle
Cylindrical and spherical
q
q
Vector algebra

## Slide 18
Notes:
Cartesian system: usually applied in the questions with surface symmetry, e.g., infinitely large surface
Cylindrical coordinates system: usually applied in the questions with axial symmetry, e.g., the field near to a charged long line.
Spherical coordinates system: usually applied in the questions with point symmetry, e.g., the field due to a point charge.

## Slide 19: 2.3 Gradient of a Scalar Field
If the quantity is a scalar，it is called scalar field;
Ex.：Temperature、Potential、Altitude…
If the quantity is a vector，it is called vector field;
Ex：Velocity of flow、Gravity、Electric、Magnetic…
If it is a function of time, it is called a time-varying field; otherwise it is called a static field.
Expression for time-varying field ：
A field is a spatial distribution of a quantity, which may or may not be a function of time.。
Scalar field and Vector field
Expression for static field ：

## Slide 20
Radar 3
Radar1
Target
Radar 2
Slowly changed
Quickly changed

## Slide 21
When the constant C take a series of different values, a series of different level surfaces will be obtained, forming the level surface family;
These surfaces fill up all the space of the scalar field；
These surfaces cannot intersect with each other.
Characteristics：
Equation：
Level surface
Level surface (line)
Level surface: Surface on which the scalar function is equal to a constant;
It describes the distribution of physical quantities in space visually.

## Slide 22
2. Directional derivative
Directional derivative: describes the spatial rate of change of a scalar field;
—— u(M) increases along line；
—— u(M) decreases along line;
—— u(M) with no change;
M0
M
Characteristics：directional derivative is related to M0 as well as line direction.
Q：What is the maximum spatial rate of change and where?
—— is directional cosines

## Slide 23
Q：which direction is the best way to skip?
Q：which direction we get the maximum change?
Gradient

## Slide 24
3. Gradient of a scalar field （ or gradu ）
Gradient of a scalar field is a vector;
Describe the maximum spatial rate of change of the scalar field at a point, and the direction of maximum value;
Direction of a gradient at some position is perpendicular to the level surface of the scalar field at the position.
The directional derivative at a position is the projection of the gradient at this position.

## Slide 25
Expression of gradient：
Cylindrical
Coordinates:
Spherical
Coordinates:
Cartesian
Coordinates:
Basic equations：

## Slide 26
Solution: (1) from the expression of gradient:
Example1
Give a scalar  (x,y,z) = x2＋y2－z, find:
(1) the gradient of  at the point P(1,1,1),
and the unit vector of that gradient;
(2) the directional derivative of  along the unit vector:
then compare the results and draw a conclusion.

## Slide 27
The unit vector of the gradient:
(2) from the relationship of the directional derivative and gradient, the directional derivative along the el:
For a certain point, the value of the directional derivative:

## Slide 28
However the gradient of that point is:
Obviously， describe the maximum value of  at the point P, the maximum directional derivative, so always is:

## Slide 29
Exercise：

## Slide 30
【浴缸放水竟产生有趣漩涡】 https://www.bilibili.com/video/BV1sd4y1J7nV/?share_source=copy_web&vd_source=c775de3b4c88257d02639e487d4cbec4
2.4 Flux and divergence of a vector field
Concept：the tangent direction of each point represents the direction of the vector field.

## Slide 31
1. Vector line
Describe the distribution of the vector field visually
Vector line equation：
Vector line
O
M

## Slide 32
2. Flux of a vector field
Q：How to quantitatively describe the size of the vector field？Flux;
and：
—— surface element；
——The normal unit vector of surface element；
—— the flux through ds.
If the surface S is closed，the direction of S is outward, the flux of the vector field on the closed surface is:
Surface element

## Slide 33
About surface element:
1. What is surface element?
A surface surrounded by a closed line/curve
Its area is small
Its direction is , it is orthogonal to the area
2. How to decide ?
For un-enclosed surface, it obeys RHR
For closed surface, outward

## Slide 34
The remained vector line is out from the closed surface
The remained vector line goes in to the closed surface
The vector line are equally in and out
three kinds of possible results:
Flux on the closed surface build the relationship between the flux of a vector field on a closed surface and the source which produce the field.
The physical meaning of flux

## Slide 35
3. Divergence of a vector field
Definition：the net outward flux of a per unit volume as the volume about the point tends to zero.

## Slide 36
Expression of divergence in
Cartesian coordinates

## Slide 37
Deduction the expression of divergence in Cartesian coordinates
The flux flowing out from the surface elements (both front and back surfaces)
let the volume element V enclosed point P to be a cube, and the field at P is F(x0, y0, z0). Using the expansion of Taylor series:
o
x
y
In Cartesian coordinates
z
z
D
x
D
y
D
P
and
is:

## Slide 38
  According to the definition of divergence：
For the same reason，flux through other surface elements could be obtained, then：

## Slide 39
Cylindrical
Coordinates:
Spherical
Coordinates:
Cartesian
Coordinates:
The expression of divergence：
The related formulas of divergence：

## Slide 40
Exercise：

## Slide 41
4. The divergence theorem
Subdivided volume
V
S1
S2
en2
en1
S
The relationship between flux and divergence：

## Slide 42: 2.5 Circulation and curl of the vector field
Circulation and vortex source of the vector field

## Slide 43
The relationship between the circulation and the current of the magnetic field：
Magnetic induction
line through the surface
Or Magnetic induction line
also runs in and out of the surface
Magnetic
induction
line

## Slide 44
The definition of circulation：
the circulation of a vector field around a closed path is defined as the scalar line integral of the vector over the path.
dl is the tangential direction of the line with much small length.
If circulation is non-zero, there exists some vortex source on the surface bounded by C。

## Slide 45
2. Curl of a vector field（ ）
（1）Circulation area density
Known as the circulation area density of vector field at the point M along the direction of
Circulation of closed curve around the unit surface element boundary:
Characteristic：The value is related to the direction of point M.

## Slide 46
The circulation area density of surface element at any orientation, is the projection of the maximum circulation area density at that point:
（2）Curl of a vector field

## Slide 47
deduction:
o
y
Dz
Dy
C
M
z
x
1
2
3
4
Expression of 、 、 in Cartesian coordinates

## Slide 48
Then
and
So

## Slide 49
The calculation formula of curl:
Cartesian
Coordinates:
Cylindrical
Coordinates:
Spherical
Coordinates:

## Slide 50
Exercise：

## Slide 51
The relevant formula of curl：
The divergence of a vector’s Curl is zero
The curl of a scalar’s gradient is zero

## Slide 54
3. Stokes's Theorem
Surface subdivision
Equally results in the opposite direction, will be cancelled by each other.
The relationship between the circulation and rotation：

## Slide 55
4. The difference of divergence and curl

## Slide 57: 2.6 Irrotational field and solenoidal field
Divergence source
Vortex source
1. Sources of vector field

## Slide 58
2. Classification of the vector field according to the field sources
（1）Irrotational field
， line integral independent with path，a conservative field。
Vector field has only divergence source without curl source:
Irrotational field can be expressed using the gradient of a scalar field:
Example：Electrostatic field

## Slide 59
（2）Solenoidal field
Vector field has only curl source without divergence source:
Feature：
Solenoidal field: can be expressed as the curl of another vector field
Example: Static magnetic field

## Slide 60
（3）Irrotational and solenoidal field
(Source is outside the discussed region)
（4）Normal field neither solenoidal nor irrotational
This field can be decomposed into two parts：irrotational part and solenoidal part;
Irrotational part
Solenoidal part

## Slide 61: 2.7 Laplacian operation
Scalar laplacian
operation
—— Laplasse
operation
Cartesian
Coordinates:
Equation：
Cylindrical
Coordinates:
Spherical
Coordinates:

## Slide 62: 2.8 Helmholtz’s Theorem
Helmholtz’s Theorem:
Where ：
In an unbounded region, a vector field is determined to within an additive constant if both its divergence and its curl are specified everywhere：

## Slide 63
Bounded area
Vector field confined within a region bounded by a surface, is determined if its divergence and curl throughout the region, as well as the normal component of the vector over the bounding face, are given.

## Slide 64: Homework
2-1, 2-2, 2-5, 2-9, 2-17, 2-20, 2-23, 2-26, 2-29, 2-32, 2-34