## Slide 1: Power Electronics
Switched Mode DC-DC Converters I:
Boost Converter, Buck-Boost Converter
Please read Chapter 7 in the textbook
  POWER ELECTRONICS
  Converters, Applications, and Design
Dr Atif Jafri
Atif.Jafri@glasgow.ac.uk

## Slide 2
The Boost Converter
  How it works?
  Important waveforms
  Expression for output voltage
    Based on average voltage of inductor
    Based on change in current of inductor
  Numerical Problems

## Slide 3
The boost converter is used to increase the output voltage (VOut) above the input voltage (VIn).
VIN
Control
Switch
D
C
RL
VOut
The boost (step-up) converter. (VOut > VIn)
If we disregard the switch for a moment and examine the circuit, we see that in the steady state the output voltage is connected to the input voltage via an inductor (assume zero resistance) and a diode. As with the buck, ignore the voltage drop across the diode.
As in the case of the buck converter we will assume the circuit operates in continuous mode, i.e., current is always flowing in the inductor.

## Slide 4
Now consider the circuit when the switch is closed.
Any voltage on capacitor C will ensure the diode is reverse biased and therefore the output circuit is “disconnected” from the input. [Because the diode’s anode is connected to ground via the switch.]
The inductor is connected across the supply (VIn) and hence current will start to build through it with the energy being stored in the magnetic field. During this phase, VL = VIn.
VIN
Control
Switch
D
C
RL
VOut
VL
Current
Switch ON: Charging the inductor !!!
VIN
Sw on
VL
Current
VL=VIn
Energy in => I ↑

## Slide 5
VIN
Control
Switch
D
C
RL
VOut
VL
Current
When the switch is opened, the inductor wants to maintain the current flow and with the supply side of the inductor still held at VIN, the potential at the opposite side of the inductor rises until the diode starts to conduct. The inductor voltage during this phase is the difference between the input voltage (VIN) and the output voltage (VOUT).
So VL = VIN – VOUT
As energy is transferred from the inductor’s magnetic field so the current flowing through the inductor and diode falls.
Switch OFF: Discharging the inductor !!!
VIN
Sw off
VOut
VL
Current
VL= VIN - VOUT
Energy out => I ↓

## Slide 6
VIN
Control
Switch
D
C
RL
VOut
±VL
Current
Shut
Open
Switch
VIN
VIN -VOUT
Inductor
voltage
Inductor current
(= supply current)
Diode current
(=output current)
Note that current always flows in the inductor (continuous mode again)
Waveforms for the boost converter

## Slide 7
Boost converter Input/Output Voltage Relation
The integral of inductor voltage is equal to the change in the inductor flux linkage.
The net change of flux linking the inductor over one time period of repetition is zero, which is a necessary condition for steady-state operation.
(
(

## Slide 8
Inductor current
Computing the change in current using following expression:
=>
When switch is closed:
Boost converter Inductor Current Change
Inductor current
(= supply current)
When switch is open:

## Slide 9
Net change in inductor current over one period is zero.
Boost converter Input/Output Voltage Relation
)
=>
Duty cycle of switching signal =
Inductor current
Inductor current
(= supply current)
=>
=>
)

## Slide 10
Minimum and Maximum Inductor Current
Note: Since change in inductor current is zero, you can take or to calculate max and min current. You need to consider the sign of the current.
Assuming lossless system

## Slide 11
Boost converter Output Voltage Ripples
Assuming that all the ripple current component of the diode current flows through the capacitor and its average value flows through the load resistor.

## Slide 12
Boost tutorial.
A boost converter has following parameters. Determine duty cycle, average, minimum and maximum inductor current and output voltage ripple.

## Slide 13
Boost tutorial.
A boost converter has following parameters. Determine duty cycle, average, minimum and maximum inductor current and output voltage ripple.

## Slide 14
Example.
A boost converter is required to provide a constant 24V / 100W output from an input voltage that varies between 9V and 15V. For a switching frequency of 20KHz and assuming 100% efficiency and operation in continuous mode, determine the following:
1. The required PWM duty cycle range to maintain a 24V DC output.
2. The average input current when the input voltage is 15V.
3. The value of the inductor required if the instantaneous current through the inductor at the end of the PWM period is zero. Calculate the value for both 9V and 15V input.
Solution:
For boost converter
=> For = 9V = 62.5%
For = 15V = 37.5%
2. Assuming 100% efficiency:

## Slide 15
3. For a boost converter. the inductor current = input current. At 15V, D=37.5% and IIN(AVE)=6.67A. We know that at the end of the PWM period the inductor current is zero, hence we can construct the current waveform:
IMAX = 13.33A
f = 20KHz, D = 37.5% => TON = 18.75μS
IAVE = 6.67A
IMAX = 2 x IAVE = 13.33A
VIN
(VIN - VOUT)
18.75μS
31.25μS
A
B

## Slide 16
The Buck-Boost Converter
  How it works?
  Important waveforms
  Expression for output voltage
    Based on average voltage of inductor
    Based on change in current of inductor
  Numerical Problems

## Slide 17
VIN
Control
Switch
D
C
RL
VOut
The buck-boost converter (VOUT <> VIN).
The Buck-Boost converter is able to produce output voltages that are higher or lower than the input voltage. Once again, we will consider the continuous mode system. Note that the output is negative with respect to the 0V side of the input voltage.
Buck-boost
VIN
0V
0V
VOUT

## Slide 18
Before starting …
… Notice that when the switch is open there is no connection between the input to the supply and its output. Hence, we can conclude that the supply is capable of delivering 0V output regardless of the input voltage for a 0% duty cycle on the switch.
With the switch closed, the input voltage is imposed across the inductor and the current through the inductor starts to rise. The diode is “off” since the cathode is more positive than the anode.
Hence for the “on” period, VL = VIN.
Note that with the diode reverse biased, the only route for the current to take that completes the circuit is back through the supply to the converter.
VIN
Control
Switch
D
C
RL
VOUT
VL
Current
Charging

## Slide 19
When the switch is opened the voltage on the inductor reverses polarity, the diode starts to conduct and hence the inductor current flows into the capacitor.
VIN
Control
Switch
D
C
RL
VOUT
VL
Current
Discharging
Note that with the switch opened there is no return path for current through the input to the converter and hence the only route the inductor current can follow is into the capacitor and load.
Also note that the capacitor will supply current to the load when there is no current contribution from the inductor.
During this “off” period, VL = VOUT and this is maintained as the current in the inductor falls to its value at the end of the PWM period.

## Slide 20
Waveforms for the buck-boost converter
OFF
ON
VIN
VOUT
Switch waveform
Inductor voltage
Inductor current
Switch current
Current INTO capacitor
ION=IL
IOFF=ICAP

## Slide 21
Buck-boost converter Input/Output Voltage Relation
Polarity is opposite than the input

## Slide 22
Inductor current
Computing the change in current using following expression:
=>
When switch is closed:
=>
When switch is open:
=>
Buck-boost converter change in inductor current

## Slide 23
Minimum and Maximum Inductor Current
Note: Since change in inductor current is zero, you can take or to calculate max and min current. You need to consider the sign of the current.
Assuming lossless system

## Slide 24
Buck-Boost converter Output Voltage Ripples
Assuming that all the ripple current component of the diode current flows through the capacitor and its average value flows through the load resistor.

## Slide 25
Question.
A small wind turbine generates 1.5V DC per MPH of wind speed.
For operation over the range 8 MPH to 32 MPH, determine the following:
1. The type of converter to be used;
2. The required range of duty cycle for these wind speeds;
3. The average input current to the converter at 32MPH;
4. The peak input current @ 32 MPH assuming operation at the boundary condition.

## Slide 26
Solution.
For a wind speed of 8MPH, the turbine output voltage is 8 x 1.5 = 12V. At a wind speed of 32 MPH the output voltage is 48V. Hence use a buck-boost converter since VIN can be less than or greater than the output voltage.
For the BB,
Neglecting the sign as it only shows the polarity with respect to input voltage.
For 8MPH, D = 24 / (12 + 24) = 66.6%
For 32 MPH, D = 24 / (48 + 24) = 33.3%

## Slide 27
Type | Voltage Equation | Current Equation
Buck (VOUT < VIN) |  | 
Boost (VOUT > VIN) |  | 
Buck-boost (VOUT <> VIN) |  | 
Converter summary
=
=

## Slide 28
Storage
Release
The following diagrams summarise the energy flow in the circuit for each converter type during the storage and release phases of operation.
Buck
Buck-boost
Buck
Boost
Buck-boost
Charging the Inductor
Discharging the Inductor
Switch ON
Switch OFF

## Slide 29: What have we learned so far?
DC-DC Converters
Switched Mode Power Supplies (Converters)
  Buck Converter
  Boost Converter
  Buck-Boost Converter